## Slide 1
  Design Issues
  Routing Algorithms
  Internetworking
  Network Layer of the Internet
Contents

## Slide 2
How do we connect different networks together?
  – This is called internetworking
  – We’ll look at how IP (Internet Protocol) does it
Internetworking

## Slide 3
Differences can be large; complicates internetworking
Internetworking

## Slide 4
Internetworking based on a common network protocol – IP
Internetworking
Packet mapped to a VC here
Common protocol (IP) carried all the way

## Slide 5
IP is the “narrow waist” of the Internet
  – Supports many different links below and apps above
Internetworking

## Slide 6
Suppose only some networks support QOS or security etc.
  – Difficult for internetwork to support
Pushes IP to be a “lowest common denominator” protocol
  – Asks little of lower-layer networks
  – Gives little as a higher layer service
Internetworking

## Slide 7
Connects two networks through a middle one
  Packets are encapsulates over the middle
Internetworking

## Slide 8
What do IP addresses look like?
  – And IP prefixes, or blocks of addresses
  – (This is IPv4; we’ll cover IPv6 later.)
IPv4 (Internet Protocol)

## Slide 9
IPv4 uses 32-bit addresses
  – Later we’ll see IPv6, which uses 128-bit addresses
Written in “dotted quad” notation
  – Four 8-bit numbers separated by dots
IPv4 (Internet Protocol)

## Slide 10
Various fields to meet straightforward needs
  Version, Header (IHL) and Total length, Protocol, and Header Checksum
IPv4 (Internet Protocol)

## Slide 11
Network layer of the Internet, uses datagrams
  – Provides a layer of addressing above link addresses (next)
IPv4 (Internet Protocol)

## Slide 12
Some fields to handle packet size differences (later)
  – Identification, Fragment offset, Fragment control bits
IPv4 (Internet Protocol)

## Slide 13
Other fields to meet other needs (later, later)
  – Differentiated Services, Time to live (TTL)
IPv4 (Internet Protocol)

## Slide 14
Addresses are allocated in blocks called prefixes
  Addresses in an L-bit prefix have the same top L bits
  Prefix is determined by the network portion
  Has 2L addresses aligned on 2L boundary
  Written address/length, e.g., 18.0.31.0/24
IP Prefixes-Modern

## Slide 15
Written in “IP address/length” notation
  – Address is lowest address in the prefix, length is prefix bits
  – E.g., 128.13.0.0/16 is 128.13.0.0 to 128.13.255.255
  – So a /24 (“slash 24”) is 256 addresses, and a /32 is one address
IP Prefixes-Modern

## Slide 16
More specific prefix
  Has longer prefix, hence a smaller number of IP addresses
Less specific prefix
  Has shorter prefix, hence a larger number of IP addresses
IP Prefixes-Modern

## Slide 17
Subnetting splits up IP prefix to help with management
  Looks like a single prefix outside the network
IP Addresses-Subnets
Network divides it into subnets internally
ISP gives network
a single prefix

## Slide 18
For IPv4, a network is also characterized by its subnet mask
Subnet masks are also expressed in dot-decimal notation like an address.
For example, 255.255.255.0 is the network mask for the 192.168.1.0/24 prefix.
IP Addresses-Subnet Mask
255.255.255.0
255.255.0.0
255.0.0.0

## Slide 19
Aggregation joins multiple IP prefixes into a single larger prefix to reduce routing table size
IP Addresses-Aggregation
ISP customers have different prefixes
ISP advertises
a single prefix

## Slide 20
Originally, IP addresses came in fixed size blocks with the class/size encoded in the high-order bits
  – They still do, but the classes are now ignored
IP Addresses

## Slide 21
Public IP addresses, e.g., 18.31.0.1
  – Valid destination on the global Internet
  – Must be allocated to you before use
  – Mostly exhausted … time for IPv6!
Private IP addresses
  – Can be used freely within private networks (home, small company)
  – 10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16
  – Need public IP address(es) and NAT to connect to global Internet
Public/Private IP addresses

## Slide 22
What is NAT (Network Address Translation)? How does it work?
  – NAT is widely used at the edges of the network, e.g., homes
Network Address Translation

## Slide 23
NAT (Network Address Translation) box maps one external IP address to many internal IP addresses
  Uses TCP/UDP port to tell connections apart
  Violates layering; very common in homes, etc.
IP Addresses-NAT

## Slide 24
Common scenario:
  Home computers use “private” IP addresses
  NAT (in AP/firewall) connects home to ISP using a single external IP address
NAT

## Slide 25
Keeps an internal/external table
  – Typically uses IP address + TCP port
  – This is address and port translation
NAT

## Slide 26
Internal to External:
  – Look up and rewrite Source IP/port
NAT

## Slide 27
External to Internal:
  – Look up and rewrite Destination IP/port
NAT

## Slide 28
Downsides:
  Connectivity has been broken!
    – Can only send incoming packets after an outgoing connection is set up
    – Difficult to run servers or peer-to-peer apps (Skype) at home
  Doesn’t work so well when there are no connections (UDP apps)
  Breaks apps that unwisely expose their IP addresses (FTP)
NAT

## Slide 29
Upsides:
  Relieves much IP address pressure
    – Many home hosts behind NATs
  Easy to deploy
    – Rapidly, and by you alone
  Useful functionality
    – Firewall, helps with privacy
  Kinks will get worked out eventually
    – “NAT Traversal” for incoming traffic
NAT

## Slide 30
Filling in the gaps we need to make for IP forwarding work in practice
  – Getting IP addresses (DHCP) ?
  – Mapping IP to link addresses (ARP) ?
ARP and DHCP

## Slide 31
Problem:
  – A node wakes up for the first time …
  – What is its IP address? What’s the IP address of its router? Etc.
  – At least Ethernet address is on NIC
Getting IP Address

## Slide 32
1. Manual configuration (old days)
  – Can’t be factory set, depends on use
2. A protocol for automatically configuring addresses (DHCP) ?
  – Shifts burden from users to IT folk
Getting IP Address

## Slide 33
DHCP (Dynamic Host Configuration Protocol), from 1993, widely used
It leases IP address to nodes
Provides other parameters too
  – Network prefix
  – Address of local router
  – DNS server, time server, etc.
DHCP

## Slide 34
DHCP Protocol Stack
DHCP is a client-server application
  – Uses UDP ports 67, 68
DHCP

## Slide 35
Bootstrap issue:
  – How does node send a message to DHCP server before it is configured?
Answer:
  – Node sends broadcast messages that delivered to all nodes on the network
  – Broadcast address is all 1s
  – IP (32 bit): 255.255.255.255
  – Ethernet (48 bit): ff:ff:ff:ff:ff:ff
DHCP

## Slide 36
DHCP

## Slide 37
Problem:
  – A node needs Link layer addresses to send a frame over the local link
  – How does it get the destination link address from a destination IP address?
Sending an IP Packet