## Slide 1
  Data Link Layer Design Issues
  Error Detection and Correction
  Elementary Data Link Protocols
  Sliding Window Protocols
  Example Data Link Protocols
Contents

## Slide 2
Responsible for delivering frames of information over a single link
  Handles transmission errors and regulates the flow of data
Physical
Link
Network
Transport
Application

## Slide 4
Link layer accepts packets from the network layer, and encapsulates them into frames that it sends using the physical layer; reception is the opposite process
Actual data path
Virtual data path
Network
Link
Physical
Frame

## Slide 5
Unacknowledged connectionless service
  Frame is sent with no connection / error recovery
  Ethernet is example
Acknowledged connectionless service
  Frame is sent with retransmissions if needed
  Example is 802.11
Acknowledged connection-oriented service
  Connection is set up; rare
Possible Services

## Slide 6
  Byte count »
  Flag bytes with byte stuffing »
  Flag bits with bit stuffing »
  Physical layer coding violations
    Use non-data symbol to indicate frame
Frame Methods

## Slide 7
Frame begins with a count of the number of bytes in it
  Simple, but difficult to resynchronize after an error
Error
case
Expected
case
Framing-Byte Count

## Slide 8
Special flag bytes delimit frames; occurrences of flags in the data must be stuffed (escaped)
  Longer, but easy to resynchronize after error
Stuffing
examples
Frame
format
Need to escape extra ESCAPE bytes too!
Framing-Byte Stuffing

## Slide 9
Stuffing done at the bit level:
  Frame flag has six consecutive 1s (not shown)
  On transmit, after five 1s in the data, a 0 is added
  On receive, a 0 after five 1s is deleted
Transmitted bits
with stuffing
Data bits
Framing-Bit Stuffing

## Slide 10
Packet over SONET(Synchronous Optical Network) is the method used to carry IP packets over SONET optical fiber links
  Uses PPP (Point-to-Point Protocol) for framing
Protocol stacks
PPP frames may be split over SONET payloads
Example Protocol: PPP

## Slide 11
IP packet
0x21 for IPv4
PPP (Point-to-Point Protocol) is a general method for delivering packets across links
  Framing uses a flag (0x7E) and (byte stuffing in Asynchronous Transmission Mode) and (bit stuffing in Synchronous Transmission Mode)
  “Unnumbered mode” (connectionless unacknowledged service) is used to carry IP packets
  Errors are detected with a checksum
Example Protocol: PPP

## Slide 12
A link control protocol brings the PPP link up/down
State machine for link control
Example Protocol: PPP

## Slide 13
Error control repairs frames that are received in error
  Requires errors to be detected at the receiver
  Typically retransmit the unacknowledged frames
  Timer protects against lost acknowledgements
Detecting errors and retransmissions are next topics.
Error Control

## Slide 14
Prevents a fast sender from out-pacing a slow receiver
  Receiver gives feedback on the data it can accept
  Rare in the Link layer as NICs run at “wire speed”
    Receiver can take data as fast as it can be sent
Flow control is a topic in the Link and Transport layers.
Flow Control

## Slide 15
Error detection codes
  Add check bits to the message bits to let some errors be detected
Error correction codes
  Add more check bits to let some errors be corrected
Key issue is now to structure the code to detect many errors with few check bits and modest computation
Error detection and Correction

## Slide 16
We want to handle more errors with less overhead
  Will look at better codes; they are applied mathematics
  But, they can’t handle all errors
  And they focus on accidental errors (will look at secure hashes later)
Error detection and Correction

## Slide 17
Error codes add structured redundancy to data so errors can be either detected, or corrected.
Error detection codes:
  Parity »
  Checksums »
  Cyclic Redundancy Codes (CRC) »
Error correction codes:
  Hamming codes »
  Binary convolutional codes »
  Reed-Solomon and Low-Density Parity Check codes
Error detection and Correction

## Slide 18
Parity bit is added as the modulo 2 sum of data bits
  Equivalent to XOR; this is even parity
  Ex: 1110000  11100001
  Detection checks if the sum is wrong (an error)
Simple way to detect an odd number of errors
  Ex: 1 error, 11100101; detected, sum is wrong
  Ex: 3 errors, 11011001; detected sum is wrong
  Ex: 2 errors, 11101101; not detected, sum is right!
  Error can also be in the parity bit itself
  Random errors are detected with probability ½
Error Detection-Parity

## Slide 19
Interleaving of N parity bits detects burst errors up to N
  Each parity sum is made over non-adjacent bits
  An even burst of up to N errors will not cause it to fail
Error Detection-Parity

## Slide 20
Checksum treats data as N-bit words and adds N check bits that are the modulo 2N sum of the words
  Ex: Internet 16-bit 1s complement checksum
Properties:
  Improved error detection over parity bits
  Detects bursts up to N errors
  Detects random errors with probability 1-2N
  Vulnerable to systematic errors, e.g., added zeros
Error Detection-Checksums

## Slide 21
Sending:
1. Arrange data in 16-bit words
2. Put zero in checksum position, add
3. Add any carryover back to get 16 bits
4. Negate (complement) to get sum
Error Detection-Checksums

## Slide 22
Receiving:
1.Arrange data in 16-bit words
2.Checksum will be non-zero, add
3.Add any carryover back to get 16 bits
4.Negate the result and check it is 0
Error Detection-Checksums

## Slide 23
Adds bits so that transmitted frame viewed as a polynomial is evenly divisible by a generator polynomial
Start by adding 0s to frame and try dividing
Offset by any reminder to make it evenly divisible
Error Detection-CRC

## Slide 24
Based on standard polynomials:
  Ex: Ethernet 32-bit CRC is defined by:
  Computed with simple shift/XOR circuits
Stronger detection than checksums:
  E.g., can detect all double bit errors
  Not vulnerable to systematic errors
Error Detection-CRC

## Slide 25
Error detection:
  – More efficient when errors are not expected
  – And when errors are large when they do occur
Error correction:
  – Needed when errors are expected
  – Or when no time for retransmission
Error Correction and Detection