## Slide 1
  Data Link Layer Design Issues
  Error Detection and Correction
  Elementary Data Link Protocols
  Example Data Link Protocols
  Retransmission
  Multiple Access
Contents

## Slide 2
Automatic Repeat reQuest (ARQ) often used when errors are common or must be corrected
  E.g., WiFi, and TCP (later)
Rules at sender and receiver:
  Receiver automatically acknowledges correct frames with an ACK
  Sender automatically resends after a timeout, until an ACK is received
Detect errors and retransmit frame

## Slide 3
Detect errors and retransmit frame
Sender
Receiver
Time
Timeout
Frame
ACK
Normal Operation (no loss)

## Slide 4
Detect errors and retransmit frame
Sender
Receiver
Time
Timeout
Frame
ACK
Loss and Retransmission
Frame

## Slide 5
Two non-trivial issues:
  How long to set the timeout?
  How to avoid accepting duplicate frames as new frames ?
Want performance in the common case and correctness always
Detect errors and retransmit frame

## Slide 6
Timeout should be:
  Not too big (link goes idle)
  Not too small (spurious resend)
Fairly easy on a LAN
  Clear worst case, little variation
Fairly difficult over the Internet
  Much variation, no obvious bound
  We’ll revisit this with TCP (later)
Detect errors and retransmit frame

## Slide 7
Detect errors and retransmit frame
Sender
Receiver
Time
Timeout
Frame
ACK
Duplicates
Frame
New frame?

## Slide 8
Detect errors and retransmit frame
Sender
Receiver
Time
Timeout
Frame
ACK
Duplicates
Frame
New frame?
ACK

## Slide 9
Frames and ACKs must both carry sequence numbers for correctness
To distinguish the current frame from the next one, a single bit (two numbers) is sufficient
  Called Stop-and-Wait
Detect errors and retransmit frame

## Slide 10
Stop and Wait
Sender
Receiver
Time
Timeout
Frame
ACK
Normal Operation (no loss)
Sender
Receiver
Time
Timeout
Frame
ACK
Frame 0
ACK 0
Frame 1
ACK 1

## Slide 11
Sender
Receiver
Time
Timeout
Frame
ACK
Duplicates (ACK Loss)
Sender
Receiver
Time
Timeout
Frame
ACK
Frame 0
ACK 0
Frame 0
ACK 0
New frame?
ACK
missing
Stop and Wait

## Slide 12
Sender
Receiver
Time
Timeout
Frame
ACK
Duplicates (early timeout)
Sender
Receiver
Time
Timeout
Frame
ACK
Frame 0
ACK 0
Frame 0
ACK 0
New frame?
Resend
Stop and Wait

## Slide 13
It allows only a single frame to be outstanding from the sender:
  Good for LAN, not efficient for high BD
Ex: R=1 Mbps, D = 50 ms
  How many frames/sec? If R=10 Mbps?
Stop and Wait

## Slide 14
Generalization of stop-and-wait
  Allows W frames to be outstanding
  Can send W frames per RTT (=2D)
  Various options for numbering frames/ACKs and handling loss
Will look at along with TCP (later)
Sliding Window

## Slide 15
How do nodes share a single link?
Who sends when, e.g., in WiFI?
  Explore with a simple model
Assume no-one is in charge; this is a distributed system
Randomized Multiple Access

## Slide 16
Seminal computer network connecting the Hawaiian islands in the late 1960s
  When should nodes send?
  A new protocol was devised by Norman Abramson …
Aloha Network
(Additive Link On-line Hawaii system)
Norman Abramson
(1932-)

## Slide 17
Simple idea:
  Node just sends when it has traffic.
  If there was a collision (no ACK received) then wait a random time and resend
Aloha Network

## Slide 18
Aloha Protocol
Collision
Collision
Time
In pure ALOHA, users transmit frames whenever they have data; users retry after a random time for collisions

## Slide 19
Aloha Protocol
Collisions happen when other users transmit during a vulnerable period that is twice the frame time
  Synchronizing senders to slots can reduce collisions

## Slide 20
Aloha Protocol
Simple, decentralized protocol that works well under low load!
Not efficient under high load
  Analysis shows at most 18% efficiency
  Improvement: divide time into slots (Slotted Aloha) and efficiency goes up to 36%

## Slide 21
ALOHA inspired Bob Metcalfe to invent Ethernet for LANs in 1973
  Nodes share 10 Mbps coaxial cable
  Hugely popular in 1980s, 1990s
Classic Ethernet
Architecture of classic Ethernet.
Bob Metcalfe
(1947-)

## Slide 22
CSMA improves on ALOHA by sensing the channel!
  User doesn’t send if it senses someone else
So does this eliminate collisions?
  Why or why not?
Variations on what to do if the channel is busy:
  1-persistent (greedy) sends as soon as idle
  Nonpersistent waits a random time then tries again
  p-persistent sends with probability p when idle
Carrier Sense Multiple Access

## Slide 23
CSMA outperforms ALOHA, and being less persistent is better under high load
Carrier Sense Multiple Access

## Slide 24
MAC protocol is 1-persistent CSMA/CD (earlier)
  Random delay (backoff) after collision is computed with BEB (Binary Exponential Backoff)
  Frame format is still used with modern Ethernet.
Ethernet
(DIX)
IEEE 802.3
Media Access Control (MAC)

## Slide 26
CSMA/CD improvement is to detect/abort collisions
  Reduced contention times improve performance
CSMA-CD (Collision Detection)
Collision time is much shorter than frame time

## Slide 27
CSMA-CD (Collision Detection)
Collision detection can take as long as 2τ

## Slide 28
Most popular LAN of the 1980s, 1990s
  10 Mbps over shared coaxial cable, with baseband signals
  Multiple access with “1-persistent CSMA/CD with BEB (Binary Exponential Backoff Algorithm)”
CSMA-CD (Collision Detection)
Architecture of classic Ethernet.

## Slide 29
CSMA-CD Performance
Efficient for large frames, even with many senders
  Degrades for small frames (and long LANs)
10 Mbps Ethernet,
64 byte min. frame

## Slide 30
Switched/Fast Ethernet
  Hubs wire all lines into a single CSMA/CD domain
  Switches isolate each port to a separate domain
    Much greater throughput for multiple ports
    No need for CSMA/CD with full-duplex lines

## Slide 31
Switched/Fast Ethernet
Switches can be wired to computers, hubs and switches
  Hubs concentrate traffic from computers
Switch
Twisted pair
Switch ports
Hub

## Slide 32
CSMA is good under low load:
  – Grants immediate access
  – Little overhead (few collisions)
But not so good under high load:
  – High overhead (expect collisions)
  – Access time varies (lucky/unlucky)
Are there other ways to eliminate collisions?
CSMA-CD (Collision Detection)

## Slide 33
They define an order in which nodes get a chance to send
  – Or pass, if no traffic at present
We just need some ordering …
  – E.g., Token Ring ?
  – E.g., node addresses
Turn-Taking Multiple Access Protocols

## Slide 34
Arrange nodes in a ring; token rotates “permission to send” to each node in turn
Token Ring
Token ring.

## Slide 35
Fixed overhead with no collisions
  More efficient under load
Regular chance to send with no unlucky nodes
  Predictable service, easily extended to guaranteed quality of service
Complexity
  More things that can go wrong than random access protocols! E.g., what if the token is lost?
  Higher overhead at low load
Turn-Taking Multiple Access Protocols

## Slide 36
How do wireless nodes share a single link? (Yes, this is WiFi!)
  Build on our simple, wired model
Wireless Multiple Access

## Slide 37
Wireless is more complicated than the wired case (Surprise!)
  Nodes may have different areas of coverage – doesn’t fit Carrier Sense ?
  Nodes can’t hear while sending – can’t Collision Detect ?
Wireless Multiple Access

## Slide 38
Wireless has complications compared to wired.
Nodes may have different coverage regions
  Leads to hidden and exposed terminals
Nodes can’t detect collisions, i.e., sense while sending
  Makes collisions expensive and to be avoided
Wireless Multiple Access

## Slide 39
Hidden terminals are senders that cannot sense each other but nonetheless collide at intended receiver
  Want to prevent; loss of efficiency
  A and C are hidden terminals when sending to B
Wireless Multiple Access

## Slide 40
Exposed terminals are senders who can sense each other but still transmit safely (to different receivers)
  Desirably concurrency; improves performance
  B  A and C  D are exposed terminals
Wireless Multiple Access

## Slide 41
MACA uses a short handshake instead of CSMA (Karn, 1990)
  802.11 uses a refinement of MACA (later)
Protocol rules:
  A sender node transmits a RTS (Request-To-Send, with frame length)
  The receiver replies with a CTS (Clear-To-Send, with frame length)
  Sender transmits the frame while nodes hearing the CTS stay silent
Multiple Access with Collision Avoidance

## Slide 42
MACA protocol grants access for A to send to B:
  A sends RTS to B [left]; B replies with CTS [right]
  A can send with exposed but no hidden terminals
Multiple Access with Collision Avoidance

## Slide 43
Wireless clients associate to a wired AP (Access Point)
  Called infrastructure mode; there is also ad-hoc mode with no AP, but that is rare.
Access Point
Client
To Network
802.11 Architecture/Protocol Stack

## Slide 44
802.11 Architecture/Protocol Stack
MAC is used across different physical layers