## Slide 1
  Theoretical Basis for Data Communications
  Guided Transmission Media
  Wireless Transmission
  Digital Modulation and Multiplexing
Contents

## Slide 2
Foundation on which other layers build
  Properties of wires, fiber, wireless limit what the network can do
Key problem is to send (digital) bits using only (analog) signals
  This is called modulation
Physical
Link
Network
Transport
Application
Modem

## Slide 3
We’ll start with an abstraction of a physical channel
Rate (or bandwidth, capacity, speed) in bits/second
Delay in seconds, related to length
Other important properties:
Whether the channel is broadcast, and its error rate
Message
Delay D
Rate R

## Slide 4
Latency is the delay to send a message over a link
– Transmission delay: time to put M-bit message “on the wire”
T-delay = M (bits) / Rate (bits/sec) = M/R seconds
– Propagation delay: time for bits to propagate across the wire
P-delay = Length / speed of signals = Length / ⅔c = D seconds
– Combining the two terms we have:

## Slide 5
The main prefixes we use:
• Use powers of 10 for rates, 2 for storage
1 Mbps = 1,000,000 bps, 1 KB = 210 bytes
• “B” is for bytes, “b” is for bits
Prefix | Exp. | Prefix | Exp.
K(ilo) | 103 | m(illi) | 10-3
M(ega) | 106 | μ(micro) | 10-6
G(iga) | 109 | n(ano) | 10-9
Notes: Deca, hector,Tera, Peta, Exa, Zetta, Yotta
Decimal
Deci, centi, pico, femto, atto, zepto, yocto

## Slide 7
1. “Dialup” with a telephone modem:
Propagation delay = 5 ms, R = 56 kbps, M = 1250 bytes
L = 5 ms + (1250 x 8) / (56 x 103) sec = 184 ms
2. Broadband cross-country link:
Propagation delay = 50 ms, R = 10 Mbps, M = 1250 bytes
L = 50 ms + (1250 x 8) / (10 x 106) sec = 51 ms
A long link or a slow rate means high latency
– Often, one delay component dominates

## Slide 8
Media have different properties, hence different performance
  Reality check
    Storage media »
  Wires:
    Twisted pairs »
    Coaxial cable »
    Power lines »
  Fiber cables »

## Slide 9
Send data on tape / disk / DVD for a high bandwidth link
  Mail one box with 1000 800GB tapes (6400 Tbit)
  Takes one day to send (86,400 secs)
  Data rate is 70 Gbps.
Data rate is faster than long-distance networks!
But, the message delay is very poor

## Slide 10
Very common; used in LANs, telephone lines
  Twists reduce radiated signal (interference)
Category 5 UTP cable with four twisted pairs
Wires – Twisted Pair

## Slide 11
Full-duplex link
  Used for transmission in both directions at once
  e.g., use different twisted pairs for each direction
Half-duplex link
  Both directions, but not at the same time
  e.g., senders take turns on a wireless channel
Simplex link
  Only one fixed direction at all times; not common
Wires – Twisted Pair

## Slide 12
Also common. Better shielding and more bandwidth for longer distances and higher rates than twisted pair.
Wires-Coaxial Cable

## Slide 13
Common for high rates and long distances
  Long distance ISP links, Fiber-to-the-Home
  Light carried in very long, thin strand of glass
Light source
(LED, laser)
Photodetector
Light trapped by
total internal reflection
Fiber

## Slide 14
Fiber has enormous bandwidth (THz) and tiny signal loss
– hence high rates over long distances
Fiber

## Slide 15
Single-mode
  Core so narrow (10um) light can’t even bounce around
  Used with lasers for long distances, e.g., 100km
Multi-mode
  Other main type of fiber
  Light can bounce (50um core)
  Used with LEDs for cheaper, shorter distance links
Fibers in a cable
Fiber

## Slide 16
Comparison of the properties of wires and fiber:
Property | Wires | Fiber
Distance | Short (100s of m) | Long (tens of km)
Bandwidth | Moderate | Very High
Cost | Inexpensive | Less cheap
Convenience | Easy to use | Less easy
Security | Easy to tap | Hard to tap
What happens to a signal as it passes over a wire?
1. The signal is delayed (propagates at ⅔c)
2. The signal is attenuated (goes for m to km)
3. Frequencies above a cutoff are highly attenuated
4. Noise is added to the signal (later, causes errors)

## Slide 17
  Electromagnetic Spectrum »
  Radio Transmission »
  Microwave Transmission »
  Light Transmission »
  Wireless vs. Wires/Fiber »
Wireless

## Slide 18
Different bands have different uses:
    Radio: wide-area broadcast; Infrared/Light: line-of-sight
    Microwave: LANs and 3G/4G/5G;
Microwave
Networking focus

## Slide 19
Fortunately, there are also unlicensed (“ISM”) bands:
    Free for use at low power; devices manage interference
    Widely used for networking; WiFi, Bluetooth, Zigbee, etc.
802.11
b/g/n
802.11a/g/n

## Slide 20
In the HF band, radio waves bounce off the ionosphere.
In the VLF, LF, and MF bands, radio waves follow the curvature of the earth
Radio signals penetrate buildings well and propagate for long distances with path loss

## Slide 21
Microwaves have much bandwidth and are widely used indoors (WiFi) and outdoors (4G, satellites)
  Signal is attenuated/reflected by everyday objects
  Strength varies with mobility due multipath fading, etc.

## Slide 22
Line-of-sight light (no fiber) can be used for links
  Light is highly directional, has much bandwidth
  Use of LEDs/cameras and lasers/photodetectors

## Slide 23
Wireless:
    Easy and inexpensive to deploy
    Naturally supports mobility
    Naturally supports broadcast
    Transmissions interfere and must be managed
    Signal strengths hence data rates vary greatly
Wires/Fiber:
    Easy to engineer a fixed data rate over point-to-point links
    Can be expensive to deploy, esp. over distances
    Doesn’t readily support mobility or broadcast